## Slide 1: T20 Cricket Game on FPGA Spartan 6
Group members:
YASEEN AHMED (21PWCSE2002)
AIMAL KHAN (21PWCSE1996)
AWAIS SADDIQUI (21PWCSE1993)
Syeda Alicia Abid (21PWCSE2086)

## Slide 2: The project aims to use FPGA's high performance and parallel processing capabilities to create an engaging and realistic cricket gaming experience. Objectives:
Efficient Hardware Utilization
Real-time Performance
Educational Tool
Unleash Real-Time Thrill
Empower Strategic Brilliance
Spark a Learning Revolution
High-Speed Gameplay
Live Player Statistics
Strategic Elements
User-Friendly Interface
Multiplayer Mode

## Slide 3: Technologies Used
Hardware: FPGA Spartan 6
Programming Language: Verilog
Development Tools: Xilinx ISE for synthesis, implementation, and simulation
Version Control: GitHub for code management and collaboration
Graphics and UI: Custom interfaces compatible with FPGA outputs, utilizing VGA or HDMI for display

## Slide 4: System Architecture
Top-Level Module: Cricket
The Cricket module is the central hub of the system, invoking the following key modules:
• debounce
• cricket_game
• bcd_display
Sub-Modules
Each sub-module has a specific role, contributing to the overall functionality of the game.
cricket_game
• Modules Called: score_and_wickets, score_comparator, led_controller
• Function: Manages the core game mechanics, including scoring, wickets, and overall game flow.
score_and_wickets
• Function: Keeps track of the current score and number of wickets.
score_comparator
• Function: Compares scores to determine the leading team or declare a win.
led_controller
• Function: Controls LED indicators based on game events such as scoring and wickets.
Debounce
• Modules Called: D_flipflop, slowClock_10Hz
• Function: Debounces the input signals to ensure noise-free button presses.
D_flipflop
• Function: Acts as a basic flip-flop for signal stabilization.
slowClock_10Hz
• Function: Generates a 10Hz clock signal for debouncing purposes.
bcd_display
• Modules Called: binary_to_BCD, slowClock_1kHz, two_bit_counter, decoder2to4, mux4to1, bcd7seg
• Function: Handles the conversion of binary scores to BCD for display purposes and manages the 7-segment display output.

## Slide 5: Development Process:
Phase 1: Initial Development
Setup Development Environment
Basic Game Logic
Simple User Interface
Phase 2: Feature Expansion
Dynamic Statistics
Advanced Gameplay Elements
Enhanced User Interface
Phase 3: Testing and Optimization
Functional Testing
Performance Optimization
Bug Fixing
Phase 4: Community Engagement
Documentation
Community Outreach
Collaborative Development
Phase 5: Launch and Dissemination
Official Launch
Marketing and Promotion
Ongoing Support

## Slide 6: Testing and Results
Functional Testing
Unit Tests
Integration Tests
System Tests
Performance Testing :
Real-time Performance
Resource Utilization
Results
Functional Validation
Performance Metrics
Input Response Time
Clock Frequency
Resource Utilization

## Slide 7: Budget and Resources :
Development Costs
Testing Equipment
Marketing and Outreach
Maintenance and Updates
Achievements
Efficient Hardware Utilization
Real-time Performance
Educational Impact
Community Engagement

## Slide 8: Future Work:
Advanced Graphics
Expanded Gameplay Features
Multiplayer Support
Portability

## Slide 9: Conclusion and Final Thoughts:
The project achieved its primary objectives, including efficient hardware utilization, real-time performance, and serving as an educational tool for FPGA programming and digital design.
By combining digital design, hardware-software integration, and real-time processing, the project not only delivers an exciting gaming experience but also serves as a valuable educational tool.